QUESTION 15.1:

- SoCalGas’ response to DRA data request DRA-JNM-01, Q.1.1, includes the workpapers to the calculation in the form of an embedded Excel worksheet.  At cell P29 of tab “SoCalGas,” which is in a column labeled “Storage Inventory Based on Excess Winter Demand (MDth)”—the contents of the cell P29 state “=((+I29+J29+K29+L29+M29)-(N29*5))+(3000*1.03)”

  - Please explain what (+I29+J29+K29+L29+M29) corresponds to.

  - Please explain what (N29*5) corresponds to.

  - Please explain why (N29*5) has been subtracted from (+I29+J29+K29+L29+M29).

  - Please explain why 3000*1.03) has been added to the formula.

RESPONSE 15.1.1:

This is year 2009 cold year winter demand (Nov 2009 through March 2010) in MDth.

RESPONSE 15.1.2:

This is the average daily core cold year demand for the April 2009 through March 2010 production year.

RESPONSE 15.1.3:

(N29*5) has been subtracted from (+I29+J29+K29+L29+M29) to calculate the amount of gas in Mdth that the winter demand shown by (+I29+J29+K29+L29+M29) is above the average cold year daily winter demand.

RESPONSE 15.1.4:

This is the calculation of the amount of peak day reliability protection gas that must be kept in inventory at the end of March of each year; i.e., 3 BCF of non-cycled gas.

QUESTION 15.2:

- SoCalGas’ response to DRA data request DRA-JNM-01, Q.1.1, includes the workpapers to the calculation in the form of an embedded Excel worksheet.  At cell P46 of tab “SDG&E,” which is in a column labeled “Storage Inventory Based on Excess Winter Demand (MDth)”—the contents of the cell P46 state “=((+I46+J46+K46+L46+M46)-(N46*5))”

  - Please explain what (+I46+J46+K46+L46+M46) corresponds to.

  - Please explain what (N46*5) corresponds to.

  - Please explain why (N46*5) has been subtracted from (+I46+J46+K46+L46+M46).

  - Comparing the formula stated in P46 of the SDG&E tab to P29 of the SoCalGas tab, please explain why the 3000*1.03 (or equivalent) factor was added to the latter formula but not to the former formula.

RESPONSE 15.2.1:

This is year 2009 cold year winter demand (Nov 2009 through March 2010) in MDth.

RESPONSE 15.2.2:

This is the average daily core cold year demand for the April 2009 through March 2010 production year.

RESPONSE 15.2.3:

(N29*5) has been subtracted from (+I29+J29+K29+L29+M29) to calculate the amount of gas in Mdth that the winter demand shown by (+I29+J29+K29+L29+M29) is above the average cold year daily winter demand.

RESPONSE 15.2.4:

The responsibility for peak day core inventory protection rests with SCG. In the past, SDG&E cycled 100% of its storage inventory while SCG was required to maintain at least 3 BCF for the core through the end of March of each year. Therefore the calculation made during the Gas Market OIR Phase II calculation reflected 100% inventory cycling for the SDG&E core.

QUESTION 15.3:

- Please provide the workpapers that support Mr. Emmrich’s calculations for Table 2 of his direct testimony in R.04-01-025, Phase 2.  Please provide these workpapers in a fully functioning Excel spreadsheet that includes all of the input data and formulas that were relied upon in developing the figures in Table 2.

RESPONSE 15.3:

QUESTION 15.4:

- Was any factor equivalent to the 3000*1.03 referred to in Q.15.1 and Q.15.1.4 included in any of the calculations supporting Table 2 as referred to in Q.15.3?

  - If yes, please identify the calculations and explain the use of the factor.

  - If no, why wasn’t the factor used in the calculations for Table 2?

RESPONSE 15.4.1:

No, this represents the 3 BCF of gas that must be maintained through March of each year for core peak day reliability protection.

RESPONSE 15.4.2:

The Gas Market OIR calculation showed the amount of storage capacity that was needed for cycling only. It was not intended to identify how much capacity the core should hold in order to cycle 69 BCF.