QUESTION SCGC-TCAP-PSEP- 18.1:

Regarding SoCalGas/SDG&E’s response to SCGC-11.3, does the reduction of MAOP from 800 psig to 640 psig over the entire length of Line 1600 put Line 1600 into Category 3?

RESPONSE SCGC-TCAP-PSEP- 18.1:

No, the pressure reduction does not qualify the pipeline as Category 3.

QUESTION SCGC-TCAP-PSEP- 18.2:

If the answer to the previous question is “no,” please explain specifically what has occurred on Line 1600 that prevents it from becoming a Category 3 pipeline.

RESPONSE SCGC-TCAP-PSEP- 18.2:

Please refer to Response SCGC-TCAP-PSEP-17.6.4.

QUESTION SCGC-TCAP-PSEP- 18.3:

Please provide the maximum recorded operating pressures on Line 1600 at Rainbow Station and as many points downstream of Rainbow as are available during the twelve months prior to the pressure drop.

RESPONSE SCGC-TCAP-PSEP- 18.3:

| Location | Max Recorded PSIG (Apr 2010 – Apr 2011) | Stationing | Recording Device |
| --- | --- | --- | --- |
| Rainbow compressor station, downstream | 794 | 1853 | Electronic pressure transmitter, Gas Control data |
| MLV* 1605 | 698 | 117800 | Electronic pressure transmitter, Gas Control data |
| MLV 1607 | 692 | 156400 | Electronic pressure transmitter, Gas Control data |
| MLV 1609 | 679 | 184400 | Electronic pressure transmitter, Gas Control data |
| MLV 1611 | 709 | 213800 | Electronic pressure transmitter, Gas Control data |
| MLV 1612 | 750 | 235200 | Electronic pressure transmitter, Gas Control data |
| MLV 1614 | 726 | 246200 | Electronic pressure transmitter, Gas Control data |
| Customer 1 | 726 | 248200 | Electronic pressure transmitter, Gas Control data |
| Mission regulator station, upstream | 726 | 261324 | Electronic pressure transmitter, Gas Control data |

* Mainline Valve

QUESTION SCGC-TCAP-PSEP- 18.4:

For each point for which SoCalGas/SDG&E provide recorded operating pressures, please identify that point using the station numbering system presented in workpaper WP-IX-1-C4 to denote the location of the recording device.

RESPONSE SCGC-TCAP-PSEP- 18.4:

Please refer to response 18.3 of this data request.

QUESTION SCGC-TCAP-PSEP- 18.5:

For each point for which SoCalGas/SDG&E provide recorded operating pressures, please identify the type of recording device and describe how and where the data is recorded.

RESPONSE SCGC-TCAP-PSEP- 18.5:

Please refer to response 18.3 of this data request.

QUESTION SCGC-TCAP-PSEP- 18.6:

For each point for which SoCalGas/SDG&E provide recorded operating pressures, please describe the facility that corresponds to the recording device.  Please indicate whether a facility provides an interconnection to a distribution system, a direct connection with a customer, an interconnection with another transmission pipeline, a regulator station, or other facility type (specify).

RESPONSE SCGC-TCAP-PSEP- 18.6:

Please refer to response 18.3 of this data request.