Title V Application Compliance Certification Materials

for Gas-Fired Equipment in the SCAQMD

INTRODUCTION

On the pages to follow are summaries and checklists to assist you in the preparation of a compliance audit and, if necessary, the resulting compliance plan.   These materials include regulatory requirements affecting natural gas use, and may be tailored to meet the needs of your facility.  If you need help or assistance, or would like to give us any comments, please call The Gas Company’s AQ AnswerLine (1-800-GAS-2000) at any time.

The spreadsheets, prepared in Excel (with file names noted in parenthesis), include the following.

For RECLAIM facilities:

Summaries -  Rule Requirements (RRules.xls), and

Audit checklists -

Facility-wide requirements (RFac.xls),

Boilers and Process Heaters (RBoil.xls),

Ovens (ROven.xls),

Internal Combustion Engines (REngine.xls), and

Gas Turbines (RTurb.xls); and

For Non-RECLAIM facilities:

Summaries -  Rule Requirements (NRRules.xls), and

Audit checklists -

Facility-wide requirements (NRFac.xls),

Boilers and Process Heaters (NRBoil.xls),

Ovens (NROven.xls),

Internal Combustion Engines (NREngine.xls), and

Gas Turbines (NRTurb.xls)

There are examples for a non-RECLAIM facility.  The first is Rule Checklist, EXRULE.XLS, and there other is an audit checklist of a boiler, EXBOIL.XLS.

DISCLAIMER

If you choose to use these materials, you must understand and agree to the following before using them:

NEITHER THE GAS COMPANY NOR YORKE ENGINEERING MAKE ANY WARRANTY OR REPRESENTATION WITH RESPECT TO THE ACCURACY, COMPLETENESS, OR UTILITY OF THIS MATERIAL AND SPECIFICALLY DISCLAIM ALL WARRANTIES, BOTH EXPRESSED AND IMPLIED, INCLUDING THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR THE INTENDED PURPOSE.  In no event shall Southern California Gas Company nor Yorke Engineering be liable for liability of any kind, including but not limited to, fines, penalties, consequential, indirect, incidental, special, or punitive damages, or loss of profits or loss of business from the use of or reliance upon these materials, even advised of the possibility of such damages.

Information in these materials is subject to change without notice.  No part of these materials may be reproduced or transmitted in any form or by any means, electronic or mechanical, for any purpose other than for compliance use at your facility, without the express written permission of Southern California Gas Company.

Copyright ( 1996 Southern California Gas Company.

All rights reserved.

Excel is a registered trademark of Microsoft Corporation.

INSTRUCTIONS

The compliance auditing spreadsheets are in Excel.  They can be easily changed and adapted to your facility’s needs.  It is very important that you review these, and modify them appropriately to incorporate rule updates, specific permit conditions, conditions specific to your facility, etc.

Step One - Customize the rule summary spreadsheets to include specific requirements for your facility.

To use these materials most effectively, first review the summary of rule requirements found in Rrules.xls. for RECLAIM facilities, or NRRules.xls, for non-RECLAIM facilities.  These summaries are based upon the rules in effect at the time of this writing - March 15, 1996.

Add additional requirements, or modify these requirements, to meet the needs of your facility.  If, in the future, the SCAQMD’s Title V guidance requires compliance with older regulations listed in the State Implementation Plan, these will have to be added.  You may wish to add requirements related to Air Toxics, Volatile Organic Compounds (VOCs), etc.  Some suggestions to add requirements are noted at the bottom of the spreadsheet.

You may also want create specific master checklists for each piece of equipment, which can be used each time you audit the euqipment.   In this case, you could delete requirements that don’t apply to that specific piece of equipment.

Also, most air districts have similar requirements; modifying the spreadsheets to conform to other air districts’ regulations would be fairly simple. (To change the headers and footers, look under File, Page Setup.)

Step Two - Customize the rule summary spreadsheets to include your specific auditing program.

Go through the summary spreadsheet and complete the last four columns:

Internal Verification Actions for Compliance Assurance,

Responsible Individual,

Verification Documentation, and

Date of Most Recent Compliance Verification.

Refer to the example provided to understand the use of these categories better.  They are intended to be a summary of your facility’s policies and procedures to maintain air quality compliance; you can modify them if others would better describe your specific situation.

Step Three - Customize the compliance checklists.

After customizing the appropriate rule summary spreadsheet, review the compliance checklists for applicability to your facility.  Modify the checklists as necessary to meet the needs of each equipment unit.  Again, some guidance to modify the checklists is noted at the bottom of the spreadsheet.  You may wish to add audit questions to assure compliance with requirements or problems that have caused violations in the past, questions that would assure compliance with permit conditions, etc.

Step Four - Conduct a compliance audit of your facility.

Complete one checklist for each unit.  After completing one checklist for every equipment unit at your facility, organize them for future reference and demonstration of your audit.  If compliance issues are identified, prepare an appropriate compliance plan, and audit the source again after a correction is made.

If you need any assistance, please call The Gas Company’s AQ AnswerLine at 1-800-GAS-2000.  We would also welcome your comments!