QUESTION DRA-DAO-29-01:

For the 3,996 wrinkle bends scheduled for replacement  during the 2012-2015 time frame, please identify the affected lines, segments (station start/stop), and segregate the lines installed before and after August 1970 in a searchable Excel format.

RESPONSE DRA-DAO-29-01:

QUESTION DRA-DAO-29-02:

Of the 385 Category 4 NTSB Criteria miles identified on page 50, how many miles are proposed to be completed in Phase 1A for SoCalGas and for SDG&E?  Are there any remaining miles scheduled for Phase 1B?

RESPONSE DRA-DAO-29-02:

The approximately 30 Category 4 Criteria Miles on L-1600 in SDG&E’s service territory are proposed to be pressure tested in Phase 1B due to the extended time that is estimated to be required to design, permit, and build and put into service the new replacement pipeline needed in order to take out of service and pressure test the existing Line 1600..  All other Category 4 Criteria miles are proposed to be addressed in Phase 1A.  However, as noted on page 60 of the Testimony, “Pipeline segments in Phase 1B are comprised of those pipeline segments that would otherwise be addressed in Phase 1A, but cannot be addressed in the near-term due to the need construct new infrastructure to maintain service during pressure testing.”  Therefore, if during the design and engineering phase of the PSEP, other Phase 1A lines are identified that cannot be tested or replaced during the Phase 1A timeframe, then those lines would be addressed in phase 1B as well.

QUESTION DRA-DAO-29-03:

Please provide the following:

- explain the difference of 385 Category 4 NTSB Criteria miles that need to be tested or replaced and the 362 miles (P. 108 identifies the 206 miles for pressure testing and P. 110 identifies 156 miles for replacement) Criteria Miles planned for Phase 1;

- identify and explain in detail the actions that have been taken to address the 23 miles difference,

- Identify the line number and segment, and explain the action plan(s) proposed for the 23 miles of Category 4 NTSB Criteria miles if not yet addressed.  Also provide the number of miles that are part of the TIMP

- Please explain the decision tree process for the 23 miles in (b) above and identify the outcomes for these lines.

RESPONSE DRA-DAO-29-03:

- The difference between the total Category 4 Criteria mileage and sum of the Category 4 Criteria mileage proposed for replacement and pressure testing is accounted for by the Category 4 Criteria mileage proposed for abandonment.

- These segments are proposed to be abandoned.

- Please reference Appendices IX-1-A through IX-1-D for the pipelines and segments with “Abandon” as the Phase 1A action item.

- Please reference the workpapers supporting Chapter IV of the testimony.  These segments have been prioritized per the Decision Tree into boxes 1 or 2.  During the review to identify the high level scope, however, it was estimated that no replacement segment would be needed.  In the case of L-41-6000-2, this line would effectively by replaced by the extension of L-6914.

QUESTION DRA-DAO-29-04:

Please answer the following questions regarding the statement on page 18 of the testimony, “Based on preliminary review of records and assumptions based on the review of pipelines located in Class 3 and 4 locations and High Consequence Areas, SoCalGas and SDG&E estimate that about an additional 2,000 miles of transmission pipeline segments will need to be assessed to determine whether they require pressure testing or replacement…”:

  - Please describe in detail the “preliminary review of records” undertaken and provide a copy of all documents used to determine that this review leads to an estimate of an additional 2,000 miles of transmission pipelines that need to be assessed.

  - Please identify the “assumptions” referenced in this statement and provide a copy of all documents and or calculations used to determine that this review leads to an estimate of an additional 2,000 miles of transmission pipelines that need to be assessed.

  - Please explain how Sempra identified the additional 2,000 miles of transmission pipelines.

  - Please state whether or not the number of Accelerated pipelines included in Phase 1A is part of the group of 2,000 miles of transmission pipelines that need to be addressed.

RESPONSE DRA-DAO-29-04:

- In D.11-06-017, the Commission concludes that “all natural gas transmission pipelines must be brought into compliance with modern standards of safety.  Historic exemptions must come to an end with an orderly and cost-conscience [sic] implementation plan.”  To effectuate that change, the Commission directed all California pipeline operators to propose plans “to comply with the requirement that all in-service natural gas transmission pipeline in California has been pressure tested in accord with 49 CFR 192.619, excluding subsection 192.619(c).  In general, pipeline installed prior to July 1, 1970 will need to be either pressure tested or replaced in order to meet this requirement.  The estimate of approximately 2,000 miles for Phase 2 was derived by making adjustments to the miles of pipeline constructed prior to 1970 by subtracting the miles proposed to be addressed in Phase 1.   
The attached PHMSA annual report has the miles of transmission line constructed by decade.  The miles from Phase 1 are summarized in Tables IV-4, IX-5, IX-7, and Table IX-14.  Accelerated replacement miles, less looping at SDG&E, is summarized in WP-IX-1-36.  Please see page WP-IX-1-57 of the workpapers supporting Chapter IX of the Testimony for the derivation of the 2,000 miles.

- It is assumed that the CPUC will require pressure testing or replacement of pipeline installed prior to 1970 since modern standards were not in place before that time.  Please see page WP-IX-1-57 of the workpapers supporting Chapter IX of the Testimony.

- Please see page WP-IX-1-57 of the workpapers supporting Chapter IX of the Testimony.

- Per the calculation detailed in the table found on page WP-IX-1-57 of the workpapers supporting Chapter IX of the Testimony, the Accelerated miles proposed to be included in the Phase 1A scope are not included in the estimated 2,000 miles of transmission pipeline segments that will need to be assessed to determine whether they require pressure testing or replacement in Phase 2.

QUESTION DRA-DAO-29-05:

Please define and provide the criteria used to determine the following terms as used by Sempra in its operations and in the PSEP filing and:

- Complete Test Records;

- Sufficient Documentation;

RESPONSE DRA-DAO-29-05:

- The phrase “complete test records” is not routinely used by Sempra in its operations and does not appear anywhere in the PSEP filing or supporting testimony.  SoCalGas and SDG&E believe the term “traceable, verifiable and complete” was used for the first time in the industry in NTSB’s January 3, 2011 safety recommendations to PG&E and the definition and applicability of this term in the natural gas industry has not yet been established.

- Page 10 of the Testimony describes one key element of the PSEP as “a plan to test or replace all pipeline segments that do not have sufficient documentation of pressure testing to satisfy the requirements of 49 CFR 192.619(a)(b) or (d).”  In this context, sufficient documentation is defined as records that include all elements required by the cited regulations.

Section IV.D of the testimony explains that in Phase 1A, SoCalGas and SDG&E prioritize those transmission pipeline segments in populated areas that do not have sufficient documentation to validate a post-construction pressure test of at least 1.25 x MAOP.  In this context, sufficient documentation can be described as at least two corroborating documents demonstrating that a 1.25 x MAOP pressure test was performed or one primary document such as a Design Data, Test Chart or Hydrotest Log.

# Footnotes

The annual DOT report was filed August 15, 2011.  The pre 1970 mileage on the report and workpaper page WP-IX-1-57 differs by 15 miles (0.6%) at SoCalGas, and 3 miles (1.8%) at SDG&E.  This discrepancy is likely due to human error.  Correction of this error does not change the estimate of approximately 2,000 miles at SoCalGas and 100 miles at SDG&E.